# Text boxes

Hold the fiber tightly. Then move stripper into the direction indicated by the arrow mark.

Edge of the coating

Press lever.

Place fiber on Single

Fiber Adapter.

The edge of the fiber coating should match with the edge of the tight holder.

Setting the fiber on the splicer

Single Fiber Adapter

Fiber Cleaving

Safety Instructions

Before operating this device, please consult the user manual for safety instructions. These guidelines will enable you to operate the product in a safe and correct manner in order to prevent harm to yourself and others.

Splicing Procedure

< Fiber Preparation >

Stripping of fiber coating

Fiber Stripper

Fiber Cleaning

Lint-free tissue with ethanol

- Turn on power.

- Select applicable program.

- Perform Arc Check.

※　Please see “Arc Check” for details.

- Insert protection sleeve.

- Prepare the fibers.

- Set fibers in splicer.

- Press  key or icon.

- Remove spliced fiber.

- Slide protection sleeve over splice point.

- Transfer fiber to heater.

- Press  key or icon.

- Remove the fiber.

End.

Select applicable heater program.

< Heater Program>

Tap the heater program area on the touchscreen, or press    key and select Heater Program

Splicer automatically feeds the fibers and discharges an arc.

Open the windshield and set the fibers.

Then enter “Arc Check”.

The result is indicated.

If the result is negative, the machine will automatically adjust the arc power. Please perform the arc check again.

An arc check is the function to adjust the arc power in order to ensure optimal splicing results. Electrode wear and environmental conditions such as temperature, humidity, and altitude, may affect the arc power.

Please perform the Arc Check at the beginning of your working day.

Arc Check

Tap the fusion program area on the touchscreen, or press    key and select Fusion Program.

Select applicable fusion program.

< Fusion Program>

Procedure for Changing Programs

Cleaning brush

< Cleaning V-groove>

To ensure optimal splicing results

Run fiber across V-groove to remove dust in V-groove.

Clean V-groove by using the cleaning brush provided or a cotton swab soaked with ethanol.

< Cleaning Fiber Clamps>

Fiber Clamp

Clean Fiber Clamps by using a cotton swab soaked with ethanol.

Maintenance

< Replacement of Electrodes>

< Cleaning Electrodes>

Electrode Sharpener

Back Side

Front Side

Remove the electrode form the electrode holder. Then replace with a new electrode.

After replacement, press the  key 10 times, after closing the windshield to remove any dust.

Stick the tip of the electrode into the electrode sharpener and turn/twist the electrode 3-4 times.

Attach the electrode holder in order from the front side to the back side.

< Cleaning Objective Lens >

Objective Lens

Remove both electrodes and V-groove.

Then clean Objective Lens by using cotton swab soaked with ethanol.

Accessory Case

Please use supplied AC adapter or optional car cigarette cable.

Power Port

Do not use an inappropriate input voltage. Doing so may cause fire, electric shock or malfunction.

FusionSplicer

Power Supply

Storage Space

Selected Splice program

Selected Heater program

Splice Process

Fiber View

Time

Battery Status

Arc Count

Menu Icon

Start Icon

Heater Start Icon

Status Icon

View Selector

Screen Indication

Power Key

Turn the power on/off.

Start Key

Start/Pause/Restart the splicing process

Heating Key

Start / Stop the heating process

Up/Down Keys

Move the cursor and change the value

Escape Key

Cancel the current action

Menu Key

Show the menu.

Enter Key

Select the menu item

Determine the value

Operation Keys